## Last commit: 2011-03-30 16:58:36 UTC by root

version 10.2R1.8;

system {

host-name EX4500;

domain-name ciccio.bello.it;

domain-search ciccio.bello.it;

authentication-order password;

root-authentication {

encrypted-password bXRe0zX1AXp1E; ## SECRET-DATA

}

name-server {

192.168.38.4;

192.168.26.30;

}

login {

user XXX {

full-name XXX;

uid 2000;

class read-only;

authentication {

encrypted-password "$1$vktJhXmX$aOXh4hVLTH.jVdZgFBe/m1"; ## SECRET-DATA

}

}

services {

ssh {

protocol-version v2;

}

netconf {

ssh;

}

web-management {

http;

}

}

syslog {

user * {

any emergency;

}

file messages {

any notice;

authorization info;

}

file interactive-commands {

interactive-commands any;

}

}

}

chassis {

aggregated-devices {

ethernet {

device-count 3;

}

}

}

interfaces {

xe-0/0/0 {

unit 0 {

family ethernet-switching {

port-mode access;

vlan {

members VLAN135;

}

}

}

}

xe-0/0/1 {

unit 0 {

family ethernet-switching {

port-mode access;

vlan {

members VLAN135;

}

}

}

}

AND ALL OTHERS PORTS …...

…................................................

ae0 {

description "TRUNK vs 3750#5-6-7";

unit 0 {

family ethernet-switching {

port-mode trunk;

vlan {

members [ default VLAN135 VLAN172 ];

}

native-vlan-id default;

}

}

}

vlan {

unit 0 {

family inet {

address 172.24.24.3/24;

}

}

unit 135 {

family inet {

address 192.168.35.254/24;

}

}

unit 172 {

family inet {

address 172.17.17.254/24;

}

}

}

}

snmp {

community public {

authorization read-only;

clients {

192.168.26.0/24;

192.168.36.0/22;

}

}

}

routing-options {

static {

route 0.0.0.0/0 next-hop 172.24.24.254;

}

}

protocols {

igmp-snooping {

vlan all;

}

rstp;

lldp {

interface all;

}

ethernet-switching-options {

inactive: secure-access-port {

interface ge-0/0/36.0 {

no-dhcp-trusted;

}

interface ge-0/0/38.0 {

no-dhcp-trusted;

}

interface xe-0/0/38.0 {

no-dhcp-trusted;

}

interface ge-0/0/39.0 {

no-dhcp-trusted;

}

interface xe-0/2/3.0 {

no-dhcp-trusted;

}

interface ae0.0 {

no-dhcp-trusted;

}

}

voip;

storm-control {

interface all;

}

}

vlans {

VLAN135 {

vlan-id 135;

l3-interface vlan.135;

}

VLAN172 {

vlan-id 172;

l3-interface vlan.172;

}

default {

description "vlan1 di gestione";

vlan-id 1;

l3-interface vlan.0;

}

}

{master:0}

root@EX4500>