## Slide 1: 128 Technology Multi-Point SVR (Multicast)

## Slide 2: Multi-POINT Introduction
2
The SENDERS send
  Multicast Addressing - rfc1700
  class D (224.0.0.0 - 239.255.255.255)‏
The RECEIVERS inform the routers what they want to receive
  Internet Group Management Protocol (IGMP) - rfc2236 -> version 2
The routers make sure the STREAMS make it to the correct receiving nets.
  Multicast Routing Protocols (PIM-SM/SSM)‏
  RPF (reverse path forwarding) – against source address

## Slide 3: Multi-POINT Introduction
3
http://www.iana.org/assignments/multicast-addresses
Examples of Reserved & Link-local Addresses
    224.0.0.0 - 224.0.0.255 reserved & not forwarded
    239.0.0.0 - 239.255.255.255 Administrative Scoping
    232.0.0.0 - 232.255.255.255 Source-Specific Multicast
    224.0.0.1 - All local hosts
    224.0.0.2 - All local routers
    224.0.0.4 - DVMRP
    224.0.0.5 - OSPF
    224.0.0.6 - Designated Router OSPF
    224.0.0.9 - RIP2
    224.0.0.13 - PIM
    224.0.0.15 - CBT
    224.0.0.18 - VRRP

## Slide 4
Multi-Point SVR

## Slide 5: Multi-POINT SVR
5
Multipoint SVR
Overlapping IP Addresses
Session Migration
UFTP Multicast / Multipoint
VLC Video Multicast / Multipoint
Joins IGMP
Bandwidth Rate-Limiting

## Slide 6: Multicast POC
Datacenter (Cheyenne, WY, USA)
Multicast Server
LAN-interface
172.16.128.1/24
Data Center Mgmt.
192.168.1.60/24
LAN x.x.x.x
Conductor Mgmt.
192.168.1.70
6
Internet
WAN1 10.0.128.1/31
SVR Secure Vector Routing
Multicast Client1
192.168.65.2
LAN-interface
192.168.65.1/24
WAN2 10.0.129.0/31
Mgmt.
192.168.1.62/24
..
Branch 2 Atlanta, GA
Multicast Client2
Multicast Client1
192.168.64.2
LAN-interface
192.168.64.1/24
WAN1 10.0.128.0/31
Mgmt.
192.168.1.61/24
..
Branch 1 Boston, MA
Multicast Client2
WAN2 10.0.129.1/31
Conductor (Minneapolis, MN)
LAN-interface
172.16.128.2/24
Meta Data Constant Flow   

## Slide 7: Multicast POC Overlapping IP Addresses
Datacenter (Cheyenne, WY, USA)
Multicast Server
LAN-interface
172.16.128.1/24
Data Center Mgmt.
192.168.1.60/24
LAN x.x.x.x
Conductor Mgmt.
192.168.1.70
7
Internet
WAN1 10.0.128.1/31
SVR Secure Vector Routing
Multicast Client1
192.168.64.2
LAN-interface
192.168.64.1/24
WAN2 10.0.129.0/31
Mgmt.
192.168.1.62/24
..
Branch 2 Atlanta, GA
Multicast Client2
Multicast Client1
192.168.64.2
LAN-interface
192.168.64.1/24
WAN1 10.0.128.0/31
Mgmt.
192.168.1.61/24
..
Branch 1 Boston, MA
Multicast Client2
WAN2 10.0.129.1/31
Conductor (Minneapolis, MN)
LAN-interface
172.16.128.2/24

## Slide 8: Multicast POC Session Migration
Datacenter (Cheyenne, WY, USA)
Multicast Server
LAN-interface
172.16.128.1/24
Data Center Mgmt.
192.168.1.60/24
LAN x.x.x.x
Conductor Mgmt.
192.168.1.70
8
Internet
WAN1 10.0.128.1/31
SVR Secure Vector Routing
Multicast Client1
192.168.65.2
LAN-interface
192.168.64.1/24
WAN2 10.0.129.0/31
Mgmt.
192.168.1.62/24
..
Branch 2 Atlanta, GA
Multicast Client2
Multicast Client1
192.168.64.2
LAN-interface
192.168.64.1/24
WAN1 10.0.128.0/31
Mgmt.
192.168.1.61/24
..
Branch 1 Boston, MA
Multicast Client2
WAN2 10.0.129.1/31
Conductor (Minneapolis, MN)
LAN-interface
172.16.128.2/24
WAN3 10.0.127.0/31
WAN4 10.0.130.0/31
WAN 3 10.0.127.1/31
WAN4 10.0.130.1/31

## Slide 9: Multicast POC Session Migration
Datacenter (Cheyenne, WY, USA)
Multicast Server
LAN-interface
172.16.128.1/24
Data Center Mgmt.
192.168.1.60/24
LAN x.x.x.x
Conductor Mgmt.
192.168.1.70
9
Internet
WAN1 10.0.128.1/31
SVR Secure Vector Routing
Multicast Client1
192.168.65.2
LAN-interface
192.168.64.1/24
WAN2 10.0.129.0/31
Mgmt.
192.168.1.62/24
..
Branch 2 Atlanta, GA
Multicast Client2
Multicast Client1
192.168.64.2
LAN-interface
192.168.64.1/24
WAN1 10.0.128.0/31
Mgmt.
192.168.1.61/24
..
Branch 1 Boston, MA
Multicast Client2
WAN2 10.0.129.1/31
Conductor (Minneapolis, MN)
LAN-interface
172.16.128.2/24
WAN3 10.0.127.0/31
WAN4 10.0.130.0/31
WAN 3 10.0.127.1/31
WAN4 10.0.130.1/31

## Slide 10: Multicast POC Failover
Mgmt.
192.168.1.61/24
..
Datacenter (Cheyenne, WY, USA)
Multicast Server
LAN-interface
172.16.128.1/24
Data Center Mgmt.
192.168.1.60/24
LAN x.x.x.x
Conductor Mgmt.
192.168.1.70
10
Internet
WAN1 10.0.128.1/31
SVR Secure Vector Routing
Multicast Client1
192.168.65.2
LAN-interface
192.168.64.1/24
WAN2 10.0.129.0/31
Mgmt.
192.168.1.62/24
..
Branch 2 Atlanta, GA
Multicast Client2
Multicast Client1
192.168.64.2
LAN-interface
192.168.64.1/24
WAN1 10.0.128.0/31
Branch 1 Boston, MA
Multicast Client2
Conductor (Minneapolis, MN)
LAN-interface
172.16.128.2/24
172.16.129.2/24
WAN3 10.0.127.0/31
WAN4 10.0.130.0/31
WAN 2 10.0.129.1/31
Datacenter2 (Santa Fe, NM, USA)
Multicast Server
LAN-interface
172.16.129.1/24
Data Center Mgmt.
192.168.1.59/24
LAN x.x.x.x
WAN 3 10.0.127.1/31
SVR Secure Vector Routing
WAN 4 10.0.130.1/31

## Slide 11: Multicast POC Failover
Mgmt.
192.168.1.61/24
..
Datacenter (Cheyenne, WY, USA)
Multicast Server
LAN-interface
172.16.128.1/24
Data Center Mgmt.
192.168.1.60/24
LAN x.x.x.x
Conductor Mgmt.
192.168.1.70
11
Internet
WAN1 10.0.128.1/31
SVR Secure Vector Routing
Multicast Client1
192.168.65.2
LAN-interface
192.168.64.1/24
WAN2 10.0.129.0/31
Mgmt.
192.168.1.62/24
..
Branch 2 Atlanta, GA
Multicast Client2
Multicast Client1
192.168.64.2
LAN-interface
192.168.64.1/24
WAN1 10.0.128.0/31
Branch 1 Boston, MA
Multicast Client2
Conductor (Minneapolis, MN)
LAN-interface
172.16.128.2/24
WAN3 10.0.127.0/31
WAN4 10.0.130.0/31
WAN 2 10.0.129.1/31
Datacenter2 (Santa Fe, NM, USA)
Multicast Server
LAN-interface
172.16.129.1/24
Data Center Mgmt.
192.168.1.59/24
LAN x.x.x.x
LAN-interface
172.16.129.2/24
WAN 3 10.0.127.1/31
SVR Secure Vector Routing
WAN 4 10.0.130.1/31

## Slide 12: Testing UFTP Multicast
UFTP Multicast
Server side can also use –H to restrict who you pass multicast to.
Uftp filename –M 230.4.5.6 –i 172.16.128.2 –t 10 (Server Side)
Client using –X5 for debugging 1-5 logging
Uftpd –d –M 230.4.5.6 –x5

## Slide 13: Testing VLC Server Multicast
Server side (VLC Receiver)
Open VLC and go to Tools  Preferences-
Then go to the bottom left corner and look for SHOW SETTINGS and click from “simple” to “All”
Then look for “Access OutPut” and change “hop limit (ttl)” from -1 to 10
In the Media menu, choose “Stream”
In the Open Media dialog file tab, click “add” and choose the file you want to stream and click “Open”
At the bottom, click the “Stream” button
This opens the “Stream Output” dialog showing the source file you have chosen. Click Next to set destination.
In “Destinations”, choose “RTP /MPEG Transport Stream” and click the “Add” button
In the “Address” box, enter the required multicast address (eg 239.255.0.1) and set the port (or leave default at 5004)
In transcoding options, choose the appropriate settings for your video and PC’s codecs. I chose “Video H.264 + MP3 (MP4)”. I had to set the options by clicking the options (screwdriver and spanner) button immediately to the right of the dropdown. In encapsulation, I chose MPEG-TS. In video codec, I set the bitrate to 4000kb/s
Once the options are set, click “Save”. Then click Next for “Option Setup” and select “Stream all elementary streams” then click stream.

## Slide 14: Testing VLC Client Multicast
Client side (VLC Receiver)
To view the stream, open another instance of VLC media player (try it on the same PC before trying it over the network)
Choose Media/Open Network Stream
2. In address, enter rtp://@239.255.0.1:5004 – choose the correct address and port you entered when setting up the stream. Don’t forget to enter the “@” symbol after “rtp://” and before the multicast ip address!
3. Click “Play”

## Slide 15: 128 Technology Multi-Point SVR (Multicast) IGMP

## Slide 16: Multi-POINT Introduction
16
The SENDERS send
  Multicast Addressing - rfc1700
  class D (224.0.0.0 - 239.255.255.255)‏
The RECEIVERS inform the routers what they want to receive
  Internet Group Management Protocol (IGMP) - rfc2236 -> version 2
The routers make sure the STREAMS make it to the correct receiving nets.
  Multicast Routing Protocols (PIM-SM/SSM)‏
  RPF (reverse path forwarding) – against source address

## Slide 17: Joining a Multicast Group
The 128T router will implement IGMPv3. IGMPv3 is backward compatible so the 128T router will be able to support clients running IGMPv1, IGMPv2, and IGMPv3. No changes will be required on clients when relying on 128T routers in the network for multicast.
Note: MLDv2 provides analogous functionality to IGMPv3 for IPv6. It will be implemented (or enabled) when IPv6 functionality is available in the 128T networking platform. IPv6 multicast functionality is beyond scope of these requirements.
The 128T router will implement IGMPv3. IGMPv3 is backward compatible so the 128T router will be able to support clients running IGMPv1, IGMPv2, and IGMPv3. No changes will be required on clients when relying on 128T routers in the network for multicast.
Note: MLDv2 provides analogous functionality to IGMPv3 for IPv6. It will be implemented (or enabled) when IPv6 functionality is available in the 128T networking platform. IPv6 multicast functionality is beyond scope of these requirements.
IGMP V2 / V3

## Slide 18: Datacenter Service Multicast Address
Unique Multicast
Specific /32 Address
No larger subnets
224.1.2.4/32
224.1.2.3/32

## Slide 19: Datacenter Service Router Multicast

## Slide 20: Datacenter Interface Multicast Configuration
Enables Sending of IGMP and MLD queries
(Multicast Listener Discovery)
Enabled (Activated)
Disabled (Deactivate)
Automatic (Activated)

## Slide 21: Multicast POC PIM / IGMP Proxy
Datacenter (Cheyenne, WY, USA)
Multicast Server
LAN-interface
172.16.128.1/24
Data Center Mgmt.
192.168.1.60/24
LAN x.x.x.x
Conductor Mgmt.
192.168.1.70
21
Internet
10.0.128.1/31
Multicast Client1
192.168.65.2
LAN-interface
192.168.65.1/24
10.0.141.1/31
Mgmt.
192.168.1.62/24
..
Branch 2 Atlanta, GA
Multicast Client2
Multicast Client1
192.168.64.2
LAN-interface
192.168.64.1/24
Mgmt.
192.168.1.61/24
..
Branch 1 Boston, MA
Multicast Client2
Conductor (Minneapolis, MN)
LAN-interface
172.16.128.2/24
PIM Relay/Proxy
PIM | IGMP Join
PIM
21
Multicast 
10.0.140.1/31
10.0.140.0/31
10.0.128.0/31
10.0.141.0/31
PIM | IGMP Join
PIM

## Slide 22: Testing VLC Client Multicast
Client side (VLC Receiver)
To view the stream, open another instance of VLC media player (try it on the same PC before trying it over the network)
Disable firewalld systemctl disable firewalld
Initiate the following command to run IGMP V2
  Echo “2” | sudo tee /proc/sys/net/ipv4/conf/eth1/force_igmp_version
Choose Media/Open Network Stream
2. In address, enter rtp://@239.255.0.1:5004 – choose the correct address and port you entered when setting up the stream. Don’t forget to enter the “@” symbol after “rtp://” and before the multicast ip address!
3. Click “Play”