## Slide 1: Juniper Apstra 4.2.1 EVE-NG Virtual Lab Demo Video series companion guide Video 9: Day-1 Core/WAN Connectivity
Colin Doyle, Sr. CE AMER
See the complete video walkthrough on YouTube at: https://www.youtube.com/@5minutejunos
Ask questions at the Juniper Elevate Community using the hashtag #5minutejunos
Adapted from v4.0.0 documentation originally compiled by: - Raymond Lam, SSE APAC - Tony Chan, SSE APAC

## Slide 2
Agenda
Day-0 Fabric Onboarding
Virtual Device Profile Verification
Virtual Device Profile Cloning
Onboarding Virtual Nodes
Create ASN Pool and IP Pools
Create Logical Devices and Interface Maps
Create Rack Types
Create Templates
Create Blueprints
Day-1 Service Provisioning
Create Routing Zones
Create Virtual Networks
Assign Virtual Network to Switchports
Add Server Links
Data Center Interconnect
DCI Addendum: Direct Peering
Core/WAN Connectivity
Internet Connectivity
Day-2 Operational Scenarios
Incorrect Cable Patch (RCA, LLDP Link Discovery, Time Voyager)
Config Deviation Checking
Apply custom config through Configlet
View Telemetry Data
Hardware Replacement
Future Documentation
Firewall Service Chaining
  Cluster with Service Block
  Type-5 Route (fabric integrated) with MNHA
VLAN Stitching
vEvo Fabric
Prepping your Lab

## Slide 3: Day-1 Service Provisioning
Create Routing Zones
Create Virtual Networks
Assign Virtual Network to Switchports
Add Testing Hosts
Data Center Interconnect (OTT)
DCI Addendum – Direct Peering
Core Connectivity
Internet Connectivity

## Slide 4
Core/WAN connectivity can be simulated using a few different methods:
Connecting your external DCI routers to additional nodes and hosts your lab
Connecting your external DCI routers to a network outside of your lab with hosts and Internet connectivity
A combination
This section of our lab will contain elements that are very specific to my (author’s) lab environment. I will make every effort to provide instructions that allow the you to understand the intent so that intent can be applied to your own lab. You may find that your own lab requires significant deviation from my specific design, but hopefully the core-concepts will remain relevant.
Core/WAN Connectivity

## Slide 5
In our example, the external DCI routers will connect to a single vSRX gateway that connects into a physical lab network. The vSRX will learn about the fabric networks using BGP and advertise those networks to an external lab firewall. This external lab firewall will provide direct connectivity to the public Internet, as well as a few other lab hosts that can be used for testing.
Core/WAN Connectivity
DC-A Blueprint
vn101 (192.168.101.0/24)
vn102 (192.168.102.0/24)
A-bms-3
ae1
ae2
A-bms-1
A-bms-2
Tenant-1 Routing Zone
DC-B Blueprint
Tenant-1 Routing Zone
ae1
B-bms-1
ae2
B-bms-2
vn101 (192.168.101.0/24)
vn103 (192.168.103.0/24)
Stretch L2 OTT DCI
192.168.102.22
192.168.101.11
192.168.101.44
192.168.103.55
192.168.101.33
External Network
HSIA

## Slide 6
As I’ve been building out this section, I’ve encountered a few other items of note that are worth calling out here at the start.
Connectivity Templates
  Method 1: Build discrete templates for DCI and Core connections
  Method 2: Combing DCI and Core connections into existing templates based on the border leaf interface they are assigned to
I can make operational arguments for both methods, so I’ll use Method 1 for DC-A, and Method 2 for DC-B. Functionally, there is no difference.
External (non-fabric/non-Apstra-managed) devices, default route advertisement, and route policy in general
I’ll do my best to explain the intent of these elements (like external DCI routers, WAN router, IGP’s, etc…) in my own lab and trust that you can apply this intent to your own environment. To keep things simple, I’m not building separate routing instances to isolate DCI and Core peering. My import/export policies are bare-minimum. I’m not using type-5 routes on external routers (this would optimize host reachability). It’s about putting just enough configuration in place to get things working. This lab is a starting point for use-case specific customization.
- Colin
Core/WAN Connectivity (a few other notes)

## Slide 7: Segmenting the DCI
Go to Blueprints > DC-A > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to Tagged, add the VLAN ID 3, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 4
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_a_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint
Method 1 (DC-A): Discrete Connectivity Templates

## Slide 8: Segmenting the DCI
Method 1 (DC-A): Discrete Connectivity Templates
Go to Blueprints > DC-A > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to Tagged, add the VLAN ID 3, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 4
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_a_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint

## Slide 9: Segmenting the DCI
Method 1 (DC-A): Discrete Connectivity Templates
Go to Blueprints > DC-A > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to Tagged, add the VLAN ID 3, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 4
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_a_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint

## Slide 10: Segmenting the DCI
Method 1 (DC-A): Discrete Connectivity Templates
Go to Blueprints > DC-A > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to Tagged, add the VLAN ID 3, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 4
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_a_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint

## Slide 11: Segmenting the DCI
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
1.
2.
3.
4.
5.
Method 1 (DC-A): Discrete Connectivity Templates
Go to Blueprints > DC-A > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to Tagged, add the VLAN ID 3, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 4
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_a_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint

## Slide 12: Segmenting the DCI
Method 1 (DC-A): Discrete Connectivity Templates
Go to Blueprints > DC-A > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to Tagged, add the VLAN ID 3, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 4
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_a_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint

## Slide 13: Updating ext-rtr1
The border leafs in DC-A are now configured to use /31 transit nets on discrete, tagged VLAN’s for connecting to ext-rtr1. To restore DCI underlay peering, we must update ext-rtr1 to use these new VLAN’s.
Log into ext-rtr1 and run the following commands (or equivalent if your lab uses different virtual nodes/interfaces/ etc…)
rename interfaces ge-0/0/1 unit 0 to unit 3
set interfaces ge-0/0/1 vlan-tagging unit 3 vlan-id 3
rename interfaces ge-0/0/2 unit 0 to unit 4
set interfaces ge-0/0/2 vlan-tagging unit 4 vlan-id 4
commit and-quit
Verify the peers come back up using “show bgp summary” from operational mode.
Method 1 (DC-A): Discrete Connectivity Templates
My original DCI transit nets did not change after updating/adding connectivity templates and committing.
NOTE: If your peers don’t come back up, go to Staged > Virtual > Protocol Sessions and verify your transit network IP’s. Because IP’s are assigned from a pool, it is possible for these to change when we modify the links/peers. If one or both change, update the Interface and BGP peer addresses on the external router.

## Slide 14: Segmenting the DCI
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to “Tagged”, add the VLAN ID 13, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 14
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_b_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint
Method 2 (DC-B): Combined Connectivity Templates

## Slide 15: Segmenting the DCI
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to “Tagged”, add the VLAN ID 13, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 14
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_b_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint
Method 2 (DC-B): Combined Connectivity Templates

## Slide 16: Segmenting the DCI
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to “Tagged”, add the VLAN ID 13, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 14
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_b_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint
Method 2 (DC-B): Combined Connectivity Templates

## Slide 17: Segmenting the DCI
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to “Tagged”, add the VLAN ID 13, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 14
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_b_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint
Method 2 (DC-B): Combined Connectivity Templates

## Slide 18: Segmenting the DCI
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to “Tagged”, add the VLAN ID 13, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 14
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_b_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
1.
3.
Method 2 (DC-B): Combined Connectivity Templates

## Slide 19: Segmenting the DCI
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct template
Change the Title to ext-router-ct_Border1
Edit the IP Link primitive, change the Interface Type to “Tagged”, add the VLAN ID 13, and click “Update”
Add a new template named ext-router-ct_Border2, and add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Default routing zone
    Interface Type: Tagged
    VLAN ID: 14
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: ext-router-policy
Unassign the ext-router-ct_Border1 template from border_rack_dc_b_001_leaf2 and assign the ext-router-ct_Border2 template, then Commit the blueprint
Method 2 (DC-B): Combined Connectivity Templates

## Slide 20: Updating ext-rtr2
The border leafs in DC-B are now configured to use /31 transit nets on discrete, tagged VLAN’s for connecting to ext-rtr1. To restore DCI underlay peering, we must update ext-rtr1 to use these new VLAN’s.
Log into ext-rtr2 and run the following commands (or equivalent if your lab uses different virtual nodes/interfaces/ etc…)
rename interfaces ge-0/0/1 unit 0 to unit 13
set interfaces ge-0/0/1 vlan-tagging unit 13 vlan-id 13
rename interfaces ge-0/0/2 unit 0 to unit 14
set interfaces ge-0/0/2 vlan-tagging unit 14 vlan-id 14
commit and-quit
Verify the peers come back up using show bgp summary from operational mode.
NOTE: If your peers don’t come back up, go to Staged > Virtual > Protocol Sessions and verify your transit network IP’s. Because IP’s are assigned from a pool, it is possible for these to change when we modify the links/peers. If one or both change, update the Interface and BGP peer addresses on the external router.
My original DCI transit nets did change after updating/adding connectivity templates and committing! I needed to update the interface and BGP peer IP’s on ext-rtr2 links to border2.
Now I need to go back and update all my lab topology screenshots. Doh!
Method 2 (DC-B): Combined Connectivity Templates

## Slide 21: Configure Core/WAN Routing Policies
Go to Blueprints > DC-A > Staged > Policies > Routing Policies and click “Create Routing Policy”
Create the policy with the following information:
  Name: core-router-policy
  Import Policy: Default
  Export Policy: L3 Edge Server Links and L2 Edge Subnets
Method 1 (DC-A): Discrete Connectivity Templates

## Slide 22: Configure the Core/WAN Routing Policies
Go to Blueprints > DC-A > Staged > Policies > Routing Policies and click “Create Routing Policy”
Create the policy with the following information:
  Name: core-router-policy
  Import Policy: Default
  Export Policy: L3 Edge Server Links and L2 Edge Subnets
Method 1 (DC-A): Discrete Connectivity Templates

## Slide 23: Configure the Core/WAN Connectivity Templates
Go to Blueprints > DC-A > Staged > Connectivity Templates and click “Add Template”
Enter the Title ext-rtr_Border1_Core, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 5
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Assign the ext-rtr_Border1_Core template to border_rack_dc_a_001_Leaf1, ge-0/0/3
Method 1 (DC-A): Discrete Connectivity Templates

## Slide 24: Configure the Core/WAN Connectivity Templates
Go to Blueprints > DC-A > Staged > Connectivity Templates and click “Add Template”
Enter the Title ext-rtr_Border1_Core, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 5
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Assign the ext-rtr_Border1_Core template to border_rack_dc_a_001_Leaf1, ge-0/0/3
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 1 (DC-A): Discrete Connectivity Templates

## Slide 25: Configure the Core/WAN Connectivity Templates
Go to Blueprints > DC-A > Staged > Connectivity Templates and click “Add Template”
Enter the Title ext-rtr_Border1_Core, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 5
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Assign the ext-rtr_Border1_Core template to border_rack_dc_a_001_Leaf1, ge-0/0/3
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 1 (DC-A): Discrete Connectivity Templates

## Slide 26: Configure the Core/WAN Connectivity Templates
Click “Add Template”
Enter the Title ext-rtr_Border2_Core, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 6
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Assign the ext-rtr_Border1_Core template to border_rack_dc_a_001_Leaf2, ge-0/0/3
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, edit the “To Generic Link IP’s” Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 1 (DC-A): Discrete Connectivity Templates

## Slide 27: Configure the Core/WAN Connectivity Templates
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 1 (DC-A): Discrete Connectivity Templates
Click “Add Template”
Enter the Title ext-rtr_Border2_Core, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 6
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Assign the ext-rtr_Border1_Core template to border_rack_dc_a_001_Leaf2, ge-0/0/3
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, edit the “To Generic Link IP’s” Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint

## Slide 28: Configure the Core/WAN Connectivity Templates
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 1 (DC-A): Discrete Connectivity Templates
Click “Add Template”
Enter the Title ext-rtr_Border2_Core, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 6
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Assign the ext-rtr_Border1_Core template to border_rack_dc_a_001_Leaf2, ge-0/0/3
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, edit the “To Generic Link IP’s” Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint

## Slide 29: Configure the Core/WAN Connectivity Templates
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 1 (DC-A): Discrete Connectivity Templates
Click “Add Template”
Enter the Title ext-rtr_Border2_Core, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 6
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Assign the ext-rtr_Border1_Core template to border_rack_dc_a_001_Leaf2, ge-0/0/3
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, edit the “To Generic Link IP’s” Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint

## Slide 30: Configure the External Router for Core/WAN Connectivity
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions and note the peer addresses for your new links
We will configure the external router to peer with the border leafs on the assigned VLAN’s and transit nets. We should see host IP’s advertised to the external router, and we will only advertise a default route into the Tenant-1 VRF. For now, this default will be a static discard. We’ll update that later when we add our upstream WAN router.
Configure ext-rtr1:
  set interfaces ge-0/0/1.5 vlan-id 5 family inet address 10.3.0.9/31
  set interfaces ge-0/0/2.6 vlan-id 6 family inet address 10.3.0.11/31
  set routing-options static route 0.0.0.0/0 discard
  set policy-options policy-statement EXPORT_DEFAULT term default from protocol static
  set policy-options policy-statement EXPORT_DEFAULT term default then accept
  set policy-options policy-statement EXPORT_DEFAULT term reject then reject
  set protocols bgp group Core export EXPORT_DEFAULT
  set protocols bgp group Core neighbor 10.3.0.8 peer-as 65102
  set protocols bgp group Core neighbor 10.3.0.10 peer-as 65103
  commit and-quit
Method 1 (DC-A): Discrete Connectivity Templates
(interfaces on ext-rtr1)

## Slide 31: Configure the External Router for Core/WAN Connectivity
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions and note the peer addresses for your new links
We will configure the external router to peer with the border leafs on the assigned VLAN’s and transit nets. We should see host IP’s advertised to the external router, and we will only advertise a default route into the Tenant-1 VRF. For now, this default will be a static discard. We’ll update that later when we add our upstream WAN router.
Configure ext-rtr1:
  set interfaces ge-0/0/1.5 vlan-id 5 family inet address 10.3.0.9/31
  set interfaces ge-0/0/2.6 vlan-id 6 family inet address 10.3.0.11/31
  set routing-options static route 0.0.0.0/0 discard
  set policy-options policy-statement EXPORT_DEFAULT term default from protocol static
  set policy-options policy-statement EXPORT_DEFAULT term default then accept
  set policy-options policy-statement EXPORT_DEFAULT term reject then reject
  set protocols bgp group Core export EXPORT_DEFAULT
  set protocols bgp group Core neighbor 10.3.0.8 peer-as 65102
  set protocols bgp group Core neighbor 10.3.0.10 peer-as 65103
  commit and-quit
Method 1 (DC-A): Discrete Connectivity Templates
NOTE: Verify your IP’s from the Protocol Sessions step from the previous slide! The transit nets I include in my router configurations may not match yours as they are being generated from a pool.
When I have problems with connecting external Generic Systems, it’s almost always because I’ve not double-checked my transit networks and I have the wrong IP’s configured!

## Slide 32: Verify External Router for Core/WAN Connectivity
Verify peers are up
  show bgp summary
Verify fabric host prefixes seen from the external router
  show route receive-protocol bgp 10.3.0.8
  show route receive-protocol bgp 10.3.0.10
Verify external router is only advertising a default route into Tenant-1
  show route advertising protocol bgp 10.3.0.8
  show route advertising protocol bgp 10.3.0.10
Test ping from router to a host
  ping 192.168.101.11
Verify default route seen in Tenant-1 on a border leaf
  (from border-leaf) show route table Tenant-1.inet.0
Method 1 (DC-A): Discrete Connectivity Templates

## Slide 33: Configure the Core/WAN Routing Policies
Go to Blueprints > DC-B > Staged > Policies > Routing Policies and click “Create Routing Policy”
Create the policy with the following information:
  Name: core-router-policy
  Import Policy: Default
  Export Policy: L3 Edge Server Links and L2 Edge Subnets
Method 2 (DC-B): Combined Connectivity Templates

## Slide 34: Configure the Core/WAN Routing Policies
Go to Blueprints > DC-B > Staged > Policies > Routing Policies and click “Create Routing Policy”
Create the policy with the following information:
  Name: core-router-policy
  Import Policy: Default
  Export Policy: L3 Edge Server Links and L2 Edge Subnets
Method 2 (DC-B): Combined Connectivity Templates

## Slide 35: Configure the Core/WAN Connectivity Templates
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct_Border1 template
Click the “Primitives” tab, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 15
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Method 2 (DC-B): Combined Connectivity Templates

## Slide 36: Configure the Core/WAN Connectivity Templates
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct_Border1 template
Click the “Primitives” tab, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 15
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 2 (DC-B): Combined Connectivity Templates

## Slide 37: Configure the Core/WAN Connectivity Templates
Go to Blueprints > DC-B > Staged > Connectivity Templates and edit the ext-router-ct_Border1 template
Click the “Primitives” tab, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 15
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 2 (DC-B): Combined Connectivity Templates

## Slide 38: Configure the Core/WAN Connectivity Templates
Edit the ext-router-ct_Border2 template
Click the “Primitives” tab, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 16
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Go to Blueprints > DC-B > Staged > Virtual > Routing Zones, edit the To Generic Link IP’s Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint
Method 2 (DC-B): Combined Connectivity Templates

## Slide 39: Configure the Core/WAN Connectivity Templates
Edit the ext-router-ct_Border2 template
Click the “Primitives” tab, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 16
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Go to Blueprints > DC-B > Staged > Virtual > Routing Zones, edit the To Generic Link IP’s Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 2 (DC-B): Combined Connectivity Templates

## Slide 40: Configure the Core/WAN Connectivity Templates
Edit the ext-router-ct_Border2 template
Click the “Primitives” tab, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 16
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Go to Blueprints > DC-B > Staged > Virtual > Routing Zones, edit the To Generic Link IP’s Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 2 (DC-B): Combined Connectivity Templates

## Slide 41: Configure the Core/WAN Connectivity Templates
Edit the ext-router-ct_Border2 template
Click the “Primitives” tab, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 16
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Go to Blueprints > DC-B > Staged > Virtual > Routing Zones, edit the To Generic Link IP’s Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 2 (DC-B): Combined Connectivity Templates

## Slide 42: Configure the Core/WAN Connectivity Templates
Edit the ext-router-ct_Border2 template
Click the “Primitives” tab, then add the IP Link, BGP Peering (Generic System), and Routing Policy primitives with the following configurations:
  IP Link
    Routing Zone: Tenant-1
    Interface Type: Tagged
    VLAN ID: 16
  BGP Peering (Generic System)
    Peer From: Interface
    Peer To: Interface/IP Endpoint
  Routing Policy
    Routing Policy: core-router-policy
Go to Blueprints > DC-B > Staged > Virtual > Routing Zones, edit the To Generic Link IP’s Resource Allocation, and assign the External Links pool to Tenant-1
Commit the Blueprint
  see the “Data Center Interconnect #1 – Underlay” section for a step-by-step walkthrough
Method 2 (DC-B): Combined Connectivity Templates

## Slide 43: Configure the External Router for Core/WAN Connectivity
Go to Blueprints > DC-B > Staged > Virtual > Protocol Sessions and note the peer addresses for your new links
We will configure the external router to peer with the border leafs on the assigned VLAN’s and transit nets. We should see host IP’s advertised to the external router, and we will only advertise a default route into the Tenant-1 VRF. For now, this default will be a static discard. We’ll update that later when we add our upstream WAN router.
Configure ext-rtr2
  set interfaces ge-0/0/1.15 vlan-id 15 family inet address 10.3.0.15/31
  set interfaces ge-0/0/2.16 vlan-id 16 family inet address 10.3.0.17/31
  set routing-options static route 0.0.0.0/0 discard
  set policy-options policy-statement EXPORT_DEFAULT term default from protocol static
  set policy-options policy-statement EXPORT_DEFAULT term default then accept
  set policy-options policy-statement EXPORT_DEFAULT term reject then reject
  set protocols bgp group Core export EXPORT_DEFAULT
  set protocols bgp group Core neighbor 10.3.0.14 peer-as 65202
  set protocols bgp group Core neighbor 10.3.0.16 peer-as 65203
  commit and-quit
Method 2 (DC-B): Combined Connectivity Templates

## Slide 44: Configure the External Router for Core/WAN Connectivity
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions and note the peer addresses for your new links
We will configure the external router to peer with the border leafs on the assigned VLAN’s and transit nets. We should see host IP’s advertised to the external router, and we will only advertise a default route into the Tenant-1 VRF. For now, this default will be a static discard. We’ll update that later when we add our upstream WAN router.
Configure ext-rtr2
  set interfaces ge-0/0/1.15 vlan-id 15 family inet address 10.3.0.15/31
  set interfaces ge-0/0/2.16 vlan-id 16 family inet address 10.3.0.17/31
  set routing-options static route 0.0.0.0/0 discard
  set policy-options policy-statement EXPORT_DEFAULT term default from protocol static
  set policy-options policy-statement EXPORT_DEFAULT term default then accept
  set policy-options policy-statement EXPORT_DEFAULT term reject then reject
  set protocols bgp group Core export EXPORT_DEFAULT
  set protocols bgp group Core neighbor 10.3.0.14 peer-as 65202
  set protocols bgp group Core neighbor 10.3.0.16 peer-as 65203
  commit and-quit
Method 2 (DC-B): Combined Connectivity Templates
NOTE: Verify your IP’s from the Protocol Sessions step from the previous slide! The transit nets I include in my router configurations may not match yours as they are being generated from a pool.
When I have problems with connecting external Generic Systems, it’s almost always because I’ve not double-checked my transit networks and I have the wrong IP’s configured!

## Slide 45: Verify External Router for Core/WAN Connectivity
Verify peers are up
  show bgp summary
Verify fabric host prefixes seen from the external router
  show route receive-protocol bgp 10.3.0.14
  show route receive-protocol bgp 10.3.0.16
Verify external router is only advertising a default route into Tenant-1
  show route advertising protocol bgp 10.3.0.14
  show route advertising protocol bgp 10.3.0.16
Test ping from router to a host
  ping 192.168.103.55
Verify default route seen in Tenant-1 on a border leaf
  (from border-leaf) show route table Tenant-1.inet.0
Method 2 (DC-B): Combined Connectivity Templates

## Slide 46: Everything Looking Good?