## Slide 1: Juniper Apstra 4.2.1 EVE-NG Virtual Lab Demo Video series companion guide Video 5: Day-1 Provisioning Services
Colin Doyle, Sr. CE AMER
See the complete video walkthrough on YouTube at: https://www.youtube.com/@5minutejunos
Ask questions at the Juniper Elevate Community using the hashtag #5minutejunos
Adapted from v4.0.0 documentation originally compiled by: - Raymond Lam, SSE APAC - Tony Chan, SSE APAC

## Slide 2
Agenda
Day-0 Fabric Onboarding
Virtual Device Profile Verification
Virtual Device Profile Cloning
Onboarding Virtual Nodes
Create ASN Pool and IP Pools
Create Logical Devices and Interface Maps
Create Rack Types
Create Templates
Create Blueprints
Day-1 Service Provisioning
Create Routing Zones
Create Virtual Networks
Assign Virtual Network to Switchports
Add Server Links
Data Center Interconnect
DCI Addendum: Direct Peering
Core/WAN Connectivity
Internet Connectivity
Day-2 Operational Scenarios
Incorrect Cable Patch (RCA, LLDP Link Discovery, Time Voyager)
Config Deviation Checking
Apply custom config through Configlet
View Telemetry Data
Hardware Replacement
Future Documentation
Firewall Service Chaining
  Cluster with Service Block
  Type-5 Route (fabric integrated) with MNHA
VLAN Stitching
vEvo Fabric
Prepping your Lab

## Slide 3: Day-1 Service Provisioning
Create Routing Zones
Create Virtual Networks
Assign Virtual Network to Switchports
Add Testing Hosts
Data Center Interconnect (OTT)
DCI Addendum – Direct Peering
Core Connectivity
Internet Connectivity

## Slide 4
A Routing Zone in Apstra is analgous to a routing-instance (VRF) in Junos. Virtual Networks (subnets) are assigned to Routing Zones when created. Like any standard network device, there is always a default instance regardless of any other VRF’s that may be created.
The below diagram illustrates the topology of the data centers after this section.
These diagrams will get more interesting, I promise!
Create Routing Zones
DC-A Blueprint
Tenant-1 Routing Zone
DC-B Blueprint
Tenant-1 Routing Zone

## Slide 5: Create Routing Zones
VRF Name | Tenant-1
VLAN ID | 10
VNI | 10010
Symmetric IRB Mode | Symmetric (enabled)
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, click “Create Routing Zone”, and create a new zone using the information in the table below

## Slide 6: Create Routing Zones
VRF Name | Tenant-1
VLAN ID | 10
VNI | 10010
Symmetric IRB Mode | Symmetric (enabled)
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, click “Create Routing Zone”, and create a new zone using the information in the table below

## Slide 7: Create Routing Zones
Repeat the previous steps to create the same Tenant-1 routing zone in DC-B
VRF Name | Tenant-1
VLAN ID | 10
VNI | 10010
Symmetric IRB Mode | Symmetric (enabled)

## Slide 8
Next, we will create two Virtual Networks (subnets) in Tenant-1.
The below diagram illustrates the topology of the data center after this section.
Create Virtual Networks
DC-A Blueprint
vn101 (192.168.101.0/24)
vn102 (192.168.102.0/24)
DC-B Blueprint
vn101 (192.168.101.0/24)
vn103 (192.168.103.0/24)
Tenant-1 Routing Zone
Tenant-1 Routing Zone

## Slide 9: Create Virtual Networks
Go go Blueprints > DC-A > Staged > Virtual > Virtual Networks and create below two virtual networks
Type | VXLAN | VXLAN
Name | vn101 | vn102
Routing Zone | Tenant-1 | Tenant-1
VNI(s) | 10101 | 10102
Reserve Across Blueprint | Yes | Yes
VLAN ID (on leafs) | 101 | 102
IPv4 Subnet | 192.168.101.0/24 | 192.168.102.0/24
Virtual Gateway IPv4 | 192.168.101.1 | 192.168.102.1
Create Connectivity Templates for | Untagged | Untagged
Assign To Rack | server_rack_dc_a_001_leaf_pair1 | server_rack_dc_a_001_leaf_pair1

## Slide 10: Create Virtual Networks
(example for vn101)
Go go Blueprints > DC-A > Staged > Virtual > Virtual Networks and create below two virtual networks
Type | VXLAN | VXLAN
Name | vn101 | vn102
Routing Zone | Tenant-1 | Tenant-1
VNI(s) | 10101 | 10102
Reserve Across Blueprint | Yes | Yes
VLAN ID (on leafs) | 101 | 102
IPv4 Subnet | 192.168.101.0/24 | 192.168.102.0/24
Virtual Gateway IPv4 | 192.168.101.1 | 192.168.102.1
Create Connectivity Templates for | Untagged | Untagged
Assign To Rack | server_rack_dc_a_001_leaf_pair1 | server_rack_dc_a_001_leaf_pair1

## Slide 11: Create Virtual Networks
Go go Blueprints > DC-A > Staged > Virtual > Virtual Networks and create below two virtual networks
Type | VXLAN | VXLAN
Name | vn101 | vn102
Routing Zone | Tenant-1 | Tenant-1
VNI(s) | 10101 | 10102
Reserve Across Blueprint | Yes | Yes
VLAN ID (on leafs) | 101 | 102
IPv4 Subnet | 192.168.101.0/24 | 192.168.102.0/24
Virtual Gateway IPv4 | 192.168.101.1 | 192.168.102.1
Create Connectivity Templates for | Untagged | Untagged
Assign To Rack | server_rack_dc_a_001_leaf_pair1 | server_rack_dc_a_001_leaf_pair1

## Slide 12: Create Virtual Networks
Go go Blueprints > DC-A > Staged > Virtual > Virtual Networks and create below two virtual networks
Type | VXLAN | VXLAN
Name | vn101 | vn102
Routing Zone | Tenant-1 | Tenant-1
VNI(s) | 10101 | 10102
Reserve Across Blueprint | Yes | Yes
VLAN ID (on leafs) | 101 | 102
IPv4 Subnet | 192.168.101.0/24 | 192.168.102.0/24
Virtual Gateway IPv4 | 192.168.101.1 | 192.168.102.1
Create Connectivity Templates for | Untagged | Untagged
Assign To Rack | server_rack_dc_a_001_leaf_pair1 | server_rack_dc_a_001_leaf_pair1

## Slide 13: Create Virtual Networks
Repeat the previous steps to create vn101 and vn103 in DC-B
Type | VXLAN | VXLAN
Name | vn101 | vn103
Routing Zone | Tenant-1 | Tenant-1
VNI(s) | 10101 | 10103
Reserve Across Blueprint | Yes | Yes
VLAN ID (on leafs) | 101 | 103
IPv4 Subnet | 192.168.101.0/24 | 192.168.103.0/24
Virtual Gateway IPv4 | 192.168.101.1 | 192.168.103.1
Create Connectivity Templates for | Untagged | Untagged
Assign To Rack | server_rack_dc_b_001_leaf_pair1 | server_rack_dc_b_001_leaf_pair1

## Slide 14: Add Routing Zone Loopback Pool
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, click the “Leaf Loopback Ips” option, and click the “Edit” button
Add DC-A Loopback to the Tenant-1 Routing Zone pool assignment
Repeat the process for DC-B, adding DC-B Loopback to Tenant-1 Routing Zone pool assignment
Commit the Blueprint for both DC-A and DC-B

## Slide 15: Add Routing Zone Loopback Pool
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, click the “Leaf Loopback Ips” option, and click the “Edit” button
Add DC-A Loopback to the Tenant-1 Routing Zone pool assignment
Repeat the process for DC-B, adding DC-B Loopback to Tenant-1 Routing Zone pool assignment
Commit the Blueprint for both DC-A and DC-B

## Slide 16: Add Routing Zone Loopback Pool
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, click the “Leaf Loopback Ips” option, and click the “Edit” button
Add DC-A Loopback to the Tenant-1 Routing Zone pool assignment
Repeat the process for DC-B, adding DC-B Loopback to Tenant-1 Routing Zone pool assignment
Commit the Blueprint for both DC-A and DC-B

## Slide 17: Add Routing Zone Loopback Pool
Go to Blueprints > DC-A > Staged > Virtual > Routing Zones, click the “Leaf Loopback Ips” option, and click the “Edit” button
Add DC-A Loopback to the Tenant-1 Routing Zone pool assignment
Repeat the process for DC-B, adding DC-B Loopback to Tenant-1 Routing Zone pool assignment
Commit the Blueprint for both DC-A and DC-B

## Slide 18
When creating a Virtual Network, an untagged connectivity template is automatically created by Apstra. Connectivity templates are where you map Virtual Networks to node interfaces that connect to Generic Systems. The auto-generated untagged connectivity templates for our Virtual Networks will be used to assign the respective untagged VLANs to switch ports.
The below diagram illustrates the topology of the data centers after this section.
Assign Virtual Network to Switchports/LAGs
DC-A Blueprint
vn101 (192.168.101.0/24)
vn102 (192.168.102.0/24)
A-bms-3
To A-leaf1
ge-0/0/9
To A-leaf2
ge-0/0/8
To A-leaf1
ge-0/0/7
To A-leaf2
ge-0/0/7
To A-leaf1
ge-0/0/8
ae1
ae2
A-bms-1_bridge
A-bms-2_bridge
vSRX
Tenant-1 Routing Zone
DC-B Blueprint
Tenant-1 Routing Zone
To B-leaf1
ge-0/0/7
To B-leaf2
ge-0/0/7
ae1
B-bms-1_bridge
vSRX
To B-leaf1
ge-0/0/8
To B-leaf2
ge-0/0/8
ae2
B-bms-2_bridge
vSRX
vn101 (192.168.101.0/24)
vn103 (192.168.103.0/24)
vSRX

## Slide 19: Assign Virtual Network to Switchports/LAGs
Go to Blueprints > DC-A > Staged > Connectivity Templates and click the “Assign” button of the connectivity template you wish to assign
Select the target interface using the table below:
Verify the status of both connectivity templates and click “Application Endpoints” to view the status
From the Application Endpoints page, you can view the assigned template for each switch ports
Update the cable map server links
  Go to Staged > Physical > Links and click the “Edit” button
  Update the links for the Generic Systems to match your lab topology
Commit the Blueprint
VN | Switch Name | Interface
vn101 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae1
 | server_rack_dc_a_001_leaf1 (Leaf) | ge-0/0/4
vn102 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae2

## Slide 20: Assign Virtual Network to Switchports/LAGs
(example shows vn101 – repeat for vn102)
Go to Blueprints > DC-A > Staged > Connectivity Templates and click the “Assign” button of the connectivity template you wish to assign
Select the target interface using the table below:
Verify the status of both connectivity templates and click “Application Endpoints” to view the status
From the Application Endpoints page, you can view the assigned template for each switch ports
Update the cable map server links
  Go to Staged > Physical > Links and click the “Edit” button
  Update the links for the Generic Systems to match your lab topology
Commit the Blueprint
VN | Switch Name | Interface
vn101 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae1
 | server_rack_dc_a_001_leaf1 (Leaf) | ge-0/0/4
vn102 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae2

## Slide 21: Assign Virtual Network to Switchports/LAGs
Go to Blueprints > DC-A > Staged > Connectivity Templates and click the “Assign” button of the connectivity template you wish to assign
Select the target interface using the table below:
Verify the status of both connectivity templates and click “Application Endpoints” to view the status
From the Application Endpoints page, you can view the assigned template for each switch ports
Update the cable map server links
  Go to Staged > Physical > Links and click the “Edit” button
  Update the links for the Generic Systems to match your lab topology
Commit the Blueprint
VN | Switch Name | Interface
vn101 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae1
 | server_rack_dc_a_001_leaf1 (Leaf) | ge-0/0/4
vn102 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae2

## Slide 22: Assign Virtual Network to Switchports/LAGs
Go to Blueprints > DC-A > Staged > Connectivity Templates and click the “Assign” button of the connectivity template you wish to assign
Select the target interface using the table below:
Verify the status of both connectivity templates and click “Application Endpoints” to view the status
From the Application Endpoints page, you can view the assigned template for each switch ports
Update the cable map server links
  Go to Staged > Physical > Links and click the “Edit” button
  Update the links for the Generic Systems to match your lab topology
Commit the Blueprint
VN | Switch Name | Interface
vn101 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae1
 | server_rack_dc_a_001_leaf1 (Leaf) | ge-0/0/4
vn102 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae2

## Slide 23: Assign Virtual Network to Switchports/LAGs
Go to Blueprints > DC-A > Staged > Connectivity Templates and click the “Assign” button of the connectivity template you wish to assign
Select the target interface using the table below:
Verify the status of both connectivity templates and click “Application Endpoints” to view the status
From the Application Endpoints page, you can view the assigned template for each switch ports
Update the cable map server links
  Go to Staged > Physical > Links and click the “Edit” button
  Update the links for the Generic Systems to match your lab topology
Commit the Blueprint
VN | Switch Name | Interface
vn101 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae1
 | server_rack_dc_a_001_leaf1 (Leaf) | ge-0/0/4
vn102 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae2

## Slide 24: Assign Virtual Network to Switchports/LAGs
Port Channel ID (ae) | Endpoint 1 (switch) | Interface | Endpoint 2 (server)
1 | server_rack_dc_a_001_leaf1 | ge-0/0/7 | server_rack_dc_a_001_sys001
2 | server_rack_dc_a_001_leaf1 | ge-0/0/8 | server_rack_dc_a_001_sys002
n/a | server_rack_dc_a_001_leaf1 | ge-0/0/9 | server_rack_dc_a_001_sys003
1 | server_rack_dc_a_001_leaf2 | ge-0/0/7 | server_rack_dc_a_001_sys001
2 | server_rack_dc_a_001_leaf2 | ge-0/0/8 | server_rack_dc_a_001_sys002
Go to Blueprints > DC-A > Staged > Connectivity Templates and click the “Assign” button of the connectivity template you wish to assign
Select the target interface using the table below:
Verify the status of both connectivity templates and click “Application Endpoints” to view the status
From the Application Endpoints page, you can view the assigned template for each switch ports
Update the cable map server links
  Go to Staged > Physical > Links and click the “Edit” button
  Update the links for the Generic Systems to match your lab topology
Commit the Blueprint
VN | Switch Name | Interface
vn101 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae1
 | server_rack_dc_a_001_leaf1 (Leaf) | ge-0/0/4
vn102 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae2

## Slide 25: Assign Virtual Network to Switchports/LAGs
Go to Blueprints > DC-A > Staged > Connectivity Templates and click the “Assign” button of the connectivity template you wish to assign
Select the target interface using the table below:
Verify the status of both connectivity templates and click “Application Endpoints” to view the status
From the Application Endpoints page, you can view the assigned template for each switch ports
Update the cable map server links
  Go to Staged > Physical > Links and click the “Edit” button
  Update the links for the Generic Systems to match your lab topology
Commit the Blueprint
VN | Switch Name | Interface
vn101 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae1
 | server_rack_dc_a_001_leaf1 (Leaf) | ge-0/0/4
vn102 | server_rack_dc_a_001_leaf1 / server_rack_dc_a_001_leaf2 (Leaf-pair) | ae2

## Slide 26: Assign Virtual Network to Switchports/LAGs
Repeat the process for DC-B and commit the Blueprint
VN | Switch Name | Interface
vn101 | server_rack_dc_b_001_leaf1 / server_rack_dc_b_001_leaf2 (Leaf-pair) | ae1
vn103 | server_rack_dc_b_001_leaf1 / server_rack_dc_b_001_leaf2 (Leaf-pair) | ae2
Port Channel ID (ae) | Endpoint 1 (switch) | Interface | Endpoint 2 (server)
1 | server_rack_dc_b_001_leaf1 | ge-0/0/7 | server_rack_dc_b_001_sys001
2 | server_rack_dc_b_001_leaf1 | ge-0/0/8 | server_rack_dc_b_001_sys002
1 | server_rack_dc_b_001_leaf2 | ge-0/0/7 | server_rack_dc_b_001_sys001
2 | server_rack_dc_b_001_leaf2 | ge-0/0/8 | server_rack_dc_b_001_sys002
Assign Virtual Networks to LAGs
Update Switchport= Assignments