SRX 650 – TWO ISP links

services {

ftp;

ssh;

telnet;

xnm-clear-text;

web-management {

management-url admin;

http {

interface [ ge-0/0/2.0 ge-0/0/3.0 vlan.823 ge-0/0/0.0 ];

}

https {

system-generated-certificate;

interface ge-0/0/2.0;

}

}

syslog {

user * {

any emergency;

}

host 122.100.122.10 {

any any;

match RT_FLOW_SESSION;

}

file messages {

any critical;

authorization info;

}

file interactive-commands {

interactive-commands error;

}

file traffic-log {

any any;

match RT_FLOW_SESSION;

}

file policy_session {

user info;

match RT_FLOW;

archive size 1000k world-readable;

structured-data;

}

}

max-configurations-on-flash 5;

max-configuration-rollbacks 5;

license {

autoupdate {

url https://ae1.juniper.net/junos/key_retrieval;

}

}

ntp {

server 149.20.68.16;

}

}

interfaces {

ge-0/0/0 {

unit 0 {

description ISP1;

family inet {

filter {

input DOWNLOAD-LIMIT;

output UPLOAD-LIMIT;

}

address 89.114.33.122/30;

address 122.100.122.249/30;

}

}

}

ge-0/0/1 {

gigether-options {

auto-negotiation;

}

}

ge-0/0/2 {

unit 0 {

family inet {

address 192.168.98.135/24;

}

}

}

ge-0/0/3 {

unit 0 {

family inet {

filter {

input filter-based-forwarding;

}

address 192.168.3.1/24;

}

}

}

ge-2/0/1 {

unit 0 {

description "Company Servers";

family inet {

address 122.100.122.1/28;

}

}

}

ge-2/0/8 {

unit 0 {

description WirelessFLEXTRUNK;

family ethernet-switching {

port-mode trunk;

vlan {

members [ WirelessNetwork FLEX ];

}

}

}

}

ge-2/0/9 {

unit 0 {

description CABLEnetCMTS;

family ethernet-switching {

port-mode access;

vlan {

members CABLEnetCMTS;

}

}

}

}

ge-2/0/10 {

unit 0 {

description CABLEnetCMTS;

family ethernet-switching {

port-mode access;

vlan {

members CABLEnetCMTS;

}

}

}

}

ge-2/0/22 {

unit 0 {

description ISP2;

family ethernet-switching {

port-mode trunk;

vlan {

members [ ISP2NET FLEX ];

}

}

}

}

ge-2/0/23 {

unit 0 {

description CABLEnetCMTS;

family ethernet-switching {

port-mode access;

vlan {

members CABLEnetCMTS;

}

}

}

}

vlan {

unit 823 {

family inet {

filter {

input riISP2;

}

address 193.91.231.98/30;

}

}

unit 824 {

family inet {

filter {

input FBFwirelles;

}

address 10.0.0.1/24;

}

}

unit 825 {

family inet {

filter {

input CMTStoISP2;

}

address 30.0.0.1/29;

}

}

}

}

routing-options {

interface-routes {

rib-group inet FBF;

}

static {

route 10.10.10.0/24 next-hop 10.0.0.11;

route 10.10.22.0/24 next-hop 10.0.0.22;

route 0.0.0.0/0 next-hop 89.114.33.121;

……………………………..

}

rib-groups {

FBF {

import-rib [ inet.0 ISP2.inet.0 ];

}

}

}

flow {

traceoptions {

file flowtrace files 5;

flag basic-datapath;

packet-filter p1 {

protocol icmp;

destination-prefix 193.91.231.98/32;

}

packet-filter p2 {

protocol icmp;

source-prefix 193.91.231.98/32;

}

}

}

screen {

ids-option untrust-screen {

icmp {

ping-death;

}

ip {

source-route-option;

tear-drop;

}

tcp {

syn-flood {

alarm-threshold 1024;

attack-threshold 200;

source-threshold 1024;

destination-threshold 2048;

timeout 20;

}

land;

}

}

}

nat {

source {

pool PublicCMTS {

address {

122.100.122.249/32;

}

}

rule-set TrustSNAT {

from zone trust;

to zone ISP2;

rule TrustSNAT {

match {

source-address 192.168.3.0/24;

destination-address 0.0.0.0/0;

}

then {

source-nat {

interface;

}

}

}

}

rule-set wirelessTOISP2 {

from zone WIRELESS;

to interface vlan.823;

rule SourceNATwireless {

match {

source-address 10.0.0.0/24;

destination-address 0.0.0.0/0;

}

then {

source-nat {

interface;

}

}

}

}

rule-set CABLE_NAT {

from zone CABLENET;

to zone ISP1;

rule noNAT {

match {

source-address [ 10.3.2.0/24 10.3.4.0/24 10.3.6.0/24 10.3.8.0/24 10.3.10.0/24 10.3.12.0/24 10.3.14.0/24 ];

destination-address 0.0.0.0/0;

}

then {

source-nat {

off;

}

}

}

rule CMTSnat {

match {

source-address [ 30.0.0.3/32 10.3.0.0/16 ];

destination-address 0.0.0.0/0;

}

then {

source-nat {

pool {

PublicCMTS;

}

}

}

}

}

rule-set CMTStoSATnat {

from zone CABLENET;

to interface vlan.823;

rule SATnat {

match {

source-address [ 10.3.2.0/24 10.3.4.0/24 10.3.6.0/24 10.3.8.0/24 10.3.10.0/24 10.3.12.0/24 10.3.14.0/24 ];

destination-address 0.0.0.0/0;

}

then {

source-nat {

interface;

}

}

}

}

}

}

policies {

from-zone trust to-zone untrust {

policy trust-to-untrust {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone trust to-zone trust {

policy trust-to-trust {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone CABLENET to-zone ISP1 {

policy cablenetTOISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

log {

session-init;

session-close;

}

}

}

}

from-zone CABLENET to-zone LAN {

policy cablenetTOlan {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone CABLENET to-zone ISP2 {

policy cablenetTOISP2 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone CABLENET to-zone PUBLICISP1 {

policy cablenetTOpublicISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone CABLENET to-zone WIRELESS {

policy cablenetTOwireless {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone PUBLICISP1 to-zone PUBLICISP1 {

policy publicISP1TOpublicISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP1 to-zone CABLENET {

policy ISP1TOcablenet {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP1 to-zone LAN {

policy ISP1TOlan {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP1 to-zone ISP2 {

policy ISP1TOISP2 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP1 to-zone PUBLICISP1 {

policy ISP1TOpublicISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP1 to-zone WIRELESS {

policy ISP1TOwireless {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone LAN to-zone CABLENET {

policy lanTOcablenet {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone LAN to-zone ISP1 {

policy lanTOISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone LAN to-zone ISP2 {

policy lanTOISP2 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone LAN to-zone PUBLICISP1 {

policy lanTOpublicISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone LAN to-zone WIRELESS {

policy lanTOwireless {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP2 to-zone CABLENET {

policy ISP2TOcablenet {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP2 to-zone ISP1 {

policy ISP2TOISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP2 to-zone LAN {

policy ISP2TOlan {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP2 to-zone PUBLICISP1 {

policy ISP2TOpublicISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP2 to-zone WIRELESS {

policy ISP2TOwireless {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone PUBLICISP1 to-zone CABLENET {

policy publicISP1TOcablenet {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone PUBLICISP1 to-zone ISP1 {

policy publicISP1TOISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

log {

session-init;

session-close;

}

}

}

}

from-zone PUBLICISP1 to-zone LAN {

policy publicISP1TOlan {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone PUBLICISP1 to-zone ISP2 {

policy publicISP1TOISP2 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone PUBLICISP1 to-zone WIRELESS {

policy publicISP1TOwireless {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone WIRELESS to-zone CABLENET {

policy wirelessTOcablenet {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone WIRELESS to-zone ISP1 {

policy wirelessTOISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone WIRELESS to-zone LAN {

policy wirelessTOlan {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone WIRELESS to-zone ISP2 {

policy wirelessTOISP2 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

log {

session-init;

session-close;

}

}

}

}

from-zone WIRELESS to-zone PUBLICISP1 {

policy wirelessTOpublicISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone trust to-zone ISP2 {

policy TrustTOSattarkt {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone LAN to-zone trust {

policy LanToTrust {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone ISP2 to-zone ISP2 {

policy STtoST {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone trust to-zone WIRELESS {

policy trustTOwireless {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone WIRELESS to-zone trust {

policy wirelessTOtrust {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone trust to-zone PUBLICISP1 {

policy trustTOpublicISP1 {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

from-zone PUBLICISP1 to-zone trust {

policy PublicISP1TOtrust {

match {

source-address any;

destination-address any;

application any;

}

then {

permit;

}

}

}

}

zones {

security-zone trust {

host-inbound-traffic {

system-services {

all;

}

protocols {

all;

}

}

interfaces {

ge-0/0/3.0;

}

}

security-zone untrust {

screen untrust-screen;

}

security-zone CABLENET {

host-inbound-traffic {

system-services {

all;

}

protocols {

all;

}

}

interfaces {

vlan.825;

ge-2/0/9.0;

ge-2/0/10.0;

ge-2/0/23.0;

}

}

security-zone ISP1 {

host-inbound-traffic {

system-services {

all;

}

protocols {

all;

}

}

interfaces {

ge-0/0/0.0;

}

}

security-zone LAN {

host-inbound-traffic {

system-services {

all;

}

protocols {

all;

}

}

interfaces {

ge-0/0/2.0;

}

}

security-zone ISP2 {

host-inbound-traffic {

system-services {

all;

}

protocols {

all;

}

}

interfaces {

vlan.823;

ge-2/0/22.0;

}

}

security-zone PUBLICISP1 {

host-inbound-traffic {

system-services {

all;

}

protocols {

all;

}

}

interfaces {

ge-2/0/2.0;

ge-2/0/3.0;

ge-2/0/4.0;

ge-2/0/5.0;

ge-2/0/6.0;

ge-2/0/7.0;

ge-2/0/1.0;

}

}

security-zone WIRELESS {

host-inbound-traffic {

system-services {

all;

}

protocols {

all;

}

}

interfaces {

vlan.824;

ge-2/0/8.0;

}

}

security-zone undefined;

}

}

firewall {

family inet {

filter FBFwirelles {

term permit {

from {

destination-address {

10.0.0.1/32;

122.100.122.0/24;

89.114.33.120/30;

}

}

then accept;

}

term toISP2 {

from {

source-address {

10.0.0.0/24;

}

}

then {

routing-instance ISP2;

}

}

term accept {

then accept;

}

}

filter CMTStoISP2 {

term permit {

from {

destination-address {

30.0.0.1/32;

}

}

then accept;

}

term toISP2 {

from {

source-address {

10.3.17.0/24;

}

}

then {

routing-instance ISP2;

}

}

term accept {

then accept;

}

}

filter riISP1 {

term riISP1 {

from {

destination-address {

193.91.231.98/32;

}

}

then {

routing-instance ISP2;

}

}

}

}

filter filter-based-forwarding {

term permit {

from {

destination-address {

192.168.3.1/32;

122.100.122.0/24;

10.0.0.0/24;

}

}

then accept;

}

term toISP2 {

from {

source-address {

192.168.3.0/24;

}

}

then {

routing-instance ISP2;

}

}

term accept {

then accept;

}

}

}

routing-instances {

ISP2 {

description route_to_ISP2;

instance-type forwarding;

routing-options {

static {

route 0.0.0.0/0 next-hop 193.91.231.97;

}

}

}

}

ethernet-switching-options {

voip;

}

vlans {

FLEX {

description FLEX;

vlan-id 909;

}

CABLEnetCMTS {

description CABLEnetCMTS;

vlan-id 11;

l3-interface vlan.825;

}

ISP2NET {

description ISP2NET;

vlan-id 823;

l3-interface vlan.823;

}rou

WirelessNetwork {

description WirelessNetwork;

vlan-id 10;

l3-interface vlan.824;

}

}